Hokuyo
URG04LX
Ultraschall
Rad Encoder
Odometrie

Data Flow

Lidar Data Converter

- Convert polar coordinates
to cartesian coordinates
- Preformat for SLAM Algo

Output:
Lidar data (1 scan) in
cartesian coordinates

Sensor Data Converter

- Convert raw Data from
Sensors/Sensor board
to usable format
for Map Generator

Output:
ulrasonic distance front
ulrasonic distance rear
relative dometry (X,Y)*
wheel encoder distance*
     * difference since last cycle

Interface Format

float scan[780][2]
Interface Format

float us_dist_front
float rel_odo_pos[2]
float we_dist

Map Generator
- SLAM
- Odometry
- Ultrasonic Sensors
- use data to generate map, determine ego position

Output:
Complete Map

Interface Format

Class: Map {
Xxx	egoPos
Xxx map
Xxx point_age

}

Path Finder

- find unknown areas in map
- convert map to readable format for
path finding algorithm (Graph?)
- calculate path (Dijkstra?) to next unknown area

Output:
Path

Data Flow

Path Converter

- Convert Path to signals for motor / steering control
-
-

Output:
Human readable signals for motor and steering
Interface Format

Motor Controller

- trigger motor and steering

Output:
PWM? ___
Interface Format
Int motor
(-900, …, +900)
Float steering
(-90, …, +90)
Motor
Steering